BOILER AB

BOILER WATER TREATMENT FOR HIGH & LOW PRESSURE BOILERS USING HARD WATER

Complete liquid treatment for steam boilers and steam condensate lines.

FEATURES:

CONVENIENT - One treatment for complete scale & corrosion control.

VERSATILE - Effective over a broad range of operating conditions.

SIMPLE TEST - Two minute drop test establishes proper dosage level.

APPLICATION:

BOILER AB is a complete liquid treatment for boilers.  This unique single package treatment contains a blend of oxygen scavengers, dispersants, alkalinity builders, and flocking agents.

DOSAGE:

Fill boiler with 12 pints of BOILER AB for every 1000 gallons of boiler water.  Estimate 10 gallons of water per horse power.  Daily dosage will depend on make-up water requirements.  Start with 4 pints of BOILER AB per 1000 gallons of make-up water.  The proper alkalinity control range is 300 to 500 ppm.

FEEDING:

Best results will be obtained feeding continuously by chemical feed pump to boiler feed water line, condensate receiver, or make-up tank.

SERVICE:

Regular service calls will be made each month.  All recommendations and adjustments for correct treatment will be discussed with operating personnel at this time.

PACKAGING:

30 gallon drums & 55 gallon drums.

"WATER TREATING CHEMICALS - WITH SERVICE"

# Text boxes

## Office: 800 - 345 – 7208

www.ryanchemical.com

# P.O. Box 406

Chandler, OK  74834

### RYAN CHEMICAL Co., Inc.