CR-496

Ryan CR-496 is highly effective for use in controlling the growth of fungi, bacteria, and algae found in industrial recirculating water cooling towers, evaporative condensers, and air washers.

PRECAUTIONARY STATEMENTS:  Hazardous to human and domestic animals.

WARNING:  Causes eye irritation.  Do not get into eyes, on skin, or on clothing.  Wear goggles or face shield, rubber gloves, and protective clothing, (hats, long sleeve shirt, and boots), when handling.  Harmful if swallowed.  Avoid contamination of food and feedstuffs.

ENVIROMENTAL HAZARDS:  This pesticide is harmful to fish.  Do not apply (or use) in estuarine oil fields where drilling fluids (muds) are discharged in to surface water.  Do not contaminate water by cleaning of equipment or disposal of wastes.  Do not discharge treated effluent into lakes, streams, ponds, or public waters unless in accordance with an NPDES permit.  For guidance contact your Regional office of the Environmental Protection Agency.

STORAGE AND DISPOSAL:

PROHIBITIONS:  Do not contaminate water, food, or feed by storage or disposal.  Open dumping is prohibited.

PESTICIDE DISPOSAL:  Pesticide wastes are toxic.  Improper disposal of excess pesticides, spray mixture, or rinsate is a violation of Federal Law.  If these wastes cannot be disposed of by use according to label instructions, contact your State Pesticide or Environmental Control Agency, or the Hazardous Waste representative at the nearest EPA Regional Office for guidance.

CONTAINER DISPOSAL:  Reseal container and offer for reconditioning.

METAL CONTAINERS:  Triple rinse (or equivalent).  Then offer for recycling or reconditioning, or puncture and dispose of in a sanitary landfill or by other approved state and local procedures.

PLASTIC CONTAINERS:  Triple rinse (or equivalent).  Then offer for recycling or reconditioning, or puncture and dispose of in a sanitary landfill, or incineration, or, if allowed by state and local authorities, by burning.  If burning, stay out of smoke.

GENERAL:  Consult federal, state, or local disposal authorities for approved alternative procedures.

DIRECTIONS FOR USE:

It is a violation of Federal Law to use this product in a manner inconsistent with its labeling.  This product must not be used on any food or field crop or to formulate any product for use on any food or field crop.

INDUSTRIAL RECIRCULATING WATER COOLING TOWERS AND EVAPORATE CONDENSERS:

Dosage for industrial recirculating water cooling towers or evaporative condensers will depend on the condition of the system prior to treatment infiltration.  Systems which are heavily contaminated should be cleaned first.  Apply Ryan CR-496 to the cleaned system or when growth is first noticed, according to the following schedule:

INITIAL DOSE:  Apply 13.06 - 43.60 ounces of product per each 1000 gallons of water in the system (120 - 400ppm).  This dose may be repeated once, twice, or three times weekly or as required to control the growth of slime-forming organisms.

SUBSEQUENT DOSE:  When microbial control is evident add 2.18 - 4.36 fluid ounces of Ryan CR-496 per 1000 gallons of water (20 - 40 ppm) in the system every three days or as needed.

AIR WASHERS:

In treating air washer systems, preclean by introducing a suitable detergent solution into the system and allow air washers to run with fan off for two hours.  Check all nozzles and manually clean those that are plugged.

FEEDING:  Ryan CR-496 may be fed directly from the drum or diluted with water and fed by any suitable feed system.  Ryan CR-496 should be dosed directly into the sump or basin or any other location where good distribution can be assured.

INITIAL DOSE:  Apply 13.06 - 21.80 ounces of product per 1000 gallons of water in the system (120 - 200ppm).  This dose may be repeated once, twice, or three times weekly or as required to control the growth of slime-forming organisms.

SUBSEQUENT DOSE:  When microbial control is evident add 2.18 - 4.36 fluid ounces of Ryan CR-496 per 1000 gallons of water (20 - 40 ppm) in the system every three days or as needed.

STATEMENT OF PRACTICAL TREATMENT:

WARNING - KEEP OUT OF REACH OF CHILDREN.  In case of contact, immediately flush eyes or skin with plenty of water for at least 15 minutes.  For eyes, call a physician.  Remove and wash contaminated clothing before reuse.  If swallowed, drink promptly a large quantity of egg whites, gelatin solution or if these are not available, drink large quantities of water.  Call a physician immediately.

ACTIVE INGREDIENTS:  Sodium Dimethyldithiocarbamate 15%.     Nabam (Disodium Ethylene Bis-dithiocarbamate) 15%.   INERT INGREDIENTS:  70.00%.     TOTAL  100.00%.

Seller makes no warranty, expressed or implied, concerning the use of this product other than indicated on the label.  Buyer assumes all risk of use and / or handling of this material, when such use and / or handling is contrary to label instructions.

"WATER TREATING CHEMICALS - WITH SERVICE"

# Text boxes

## Office: 800 - 345 – 7208

www.ryanchemical.com

# P.O. Box 406

Chandler, OK  74834

### RYAN CHEMICAL Co., Inc.