R-862

DIRECTIONS FOR USE:

It is a violation of federal law to use this product in a manner inconsistent with its labeling.

NOTE:  Add separately to the system.  Do not mix with other additives to avoid possible incompatibilities.

OPEN RECIRCULATING COOLING SYSTEM:

INITIAL DOSE:  When microbiological slimes are evident, apply 9.3 to 18.6 fluid ounces per 1000 gallons of water in the system.  Repeat until control is achieved.  Badly fouled systems should be cleansed before treatment is begun.

SUBSEQUENT DOSE:  When microbiological control is evident, apply 6.2 to 12.4 fluid ounces per 1000 gallons of water in the system once per week, or as needed to maintain control.

FEEDING:  Should be fed at full strength in the cooling tower basin at a point of maximum water circulating.  Tower bleed off valves should be closed to permit a retention time of 4 hours.

PAPER MILLS:  Dosage will vary from 4.8 to 9.6 fluid ounces per ton of finished paper depending on the type of stock, complexity of the system, quality of raw water, and type and degrees of contamination.

FEEDING:  May be drip fed continuously from the drum or led by suitable chemical pumps such as adjustable proportioning types; variable speed, positive displacement type; or by the reciprocating type.  This product should be fed as early as possible in the system at such points including the hydropulper, machine chest, or broke system.

PRECAUTIONARY STATEMENTS                                     DANGER                                      HAZARDS TO HUMANS AND DOMESTIC ANIMALS:

Corrosive.  Causes eye damage and skin irritation.  May be absorbed through the skin.  Do not get in eyes, on skin or clothing.  Wear goggles and rubber gloves when handling.  Harmful or fatal if swallowed.  Avoid contamination with food.  Water treated with this product should not be used for food processing, irrigation, or in the manufacture of paper used for food packaging.

STATEMENT OF PRACTICAL TREATMENT:

In case of skin contact, wash with plenty of soap and water.  For eyes, flush with water for 15 minutes and get prompt medical attention.  Remove and wash contaminated clothing before reuse.  If swallowed, drink promptly a large quantity of milk, egg whites, gelatin solution or if these are not available, drink large quantities of water.  Avoid alcohol.  Call a physician immediately.

NOTE TO PHYSICIAN:  Probable mucosal damage may contraindicate the use of gastric lavage.  Measures against circulatory shock, respiratory depression and convulsion may be needed.

ENVIROMENTAL HAZARDS:

This pesticide is toxic to fish.  Do not discharge effluent containing this product into lakes, streams, ponds, estuaries, oceans, or public waters unless this product is specifically identified and addressed in an NPDES permit.  Do not discharge effluent containing this product to sewer systems without previously notifying the sewage treatment plant authority.  For guidance contact your State Water Board or Regional Office of the EPA.

PHYSICAL AND CHEMICAL HAZARDS:

This is a cationic germicide.  Do not mix with soap or anionic materials.

STORAGE AND DISPOSABLE:

This product must be kept under locked storage sufficient to make it inaccessible to children or persons unfamiliar with its proper use.  Do not contaminate water, food, or feed by storage or disposal.  Open dumping is prohibited.  Do not reuse empty container.

PESTICIDE DISPOSAL:

Pesticide wastes are acutely hazardous.  Improper disposal of excess pesticide, spray mixture, or rinsate is a violation of federal law.  If these wastes cannot be disposed of by use according to label instructions, contact your State Pesticide or Environmental Control Agency, or the Hazardous Waste representative at the nearest EPA Regional Office for guidance.

CONTAINER DISPOSAL:

PLASTIC CONTAINERS - Triple rinse (or equivalent), then offer recycling or reconditioning, or puncture and dispose of in a sanitary landfill, or incineration, or, if allowed by state or local authorities, by burning.  If burned, stay out of smoke.

FIBER DRUMS WITH LINERS - Completely empty liner by shaking and tapping sides and bottom to loosen clinging particles.  Empty residue into application equipment.  Then dispose of liner in a sanitary landfill or by incineration if allowed by state and local authorities.  If drum is contaminated and cannot be reused, dispose of in the same manner.

METAL CONTAINERS - Triple rinse (or equivalent).  Then offer for recycling or reconditioning, or puncture and dispose of in a sanitary landfill, or by other procedures as approved by state and local authorities.

ACTIVE INGREDIENTS:

n-Alkyl (60% C14 , 5% C12 , 30% C16 , 5% C18)   dimethyl benzyl ammonium chloride 12.50%   bis (tri-n-butyltin) oxide  2.25 %.

INERT INGREDIENTS:  85.25%       TOTAL  100.00%

KEEP OUT OF REACH OF CHILDREN                   EPA REG. NO. 47371-29  EPA EST. NO. 50640

"WATER TREATING CHEMICALS - WITH SERVICE"

# Text boxes

## Office: 800 - 345 – 7208

www.ryanchemical.com

# P.O. Box 406

Chandler, OK  74834

### RYAN CHEMICAL Co., Inc.