RT-86

MULTIPURPOSE SCALE AND CORROSION INHIBITOR

FEATURES:

CONTROLS CORROSION - Highly effective inhibitor even at elevated temperatures.

CONTROLS SCALE AND FOULING - Unique combination of sequesterants and

dispersants to keep heat exchange surfaces clean.

NON-POLLUTING - Contains no zinc or other heavy metals.

ELIMINATES ACID FEED - Separate acid feed not required.

ECONOMICAL AND CONVENIENT - Complete liquid treatment can be fed direct from

the drum.

APPLICATION:

RT-86 cooling water treatment is recommended for use in air conditioning systems, air wash systems and other open recirculating cooling water systems.  RT-86 is a multipurpose scale inhibitor and antifoulant.  The unique combination of inhibitors in RT-86 protects steel, copper, and copper alloy system metals.  The excellent corrosion inhibitor combination in RT-86 allows it to be used even at elevated temperatures (>110 degrees F.).  Superior corrosion inhibition is provided by the antifoulant / sequesterant combination, which allows maximum contact between the inhibitor and metal surfaces.

DOSAGE:

The recommended dosage range for RT-86 is 12 to 20 ppm, in the recirculating water.  Approximately 1-2 pints of RT-86 for each 1000 gallons of make-up water should be fed or 1-2 quarts per 100 tons daily.  Systems operating over 110 degrees F. will require the higher dosage level.

HANDLING:

Harmful if swallowed.  Do not use in potable water systems.  Alkaline solution.  Avoid prolonged or repeated contact.  Flush from skin with water.  If eyes are affected, flush thoroughly with water and get prompt medical attention.  Keep container closed when not in use.

FEEDING:

RT-86 may be pumped directly from the drum into a recirculating cooling water line or directly to the tower basin.  A proportional feed and bleed system controlled by a monitor or a make-up water meter is recommended.

BLEED-OFF:

A Ryan representative will recommend the proper bleed-off, according to individual specifications of the units to be treated.

SERVICE:

Regular service calls will be made by a Ryan representative.  Recommendations for changes in the treatment program will be made as the individual situation warrants.

PACKAGING:

5 gallon containers, 30 gallon drums, & 55 gallon drums.

"WATER TREATING CHEMICALS - WITH SERVICE"

# Text boxes

## Office: 800 - 345 – 7208

www.ryanchemical.com

# P.O. Box 406

Chandler, OK  74834

### RYAN CHEMICAL Co., Inc.