RWT-32AD

COOLING WATER TREATMENT (Non-Acid Type)

A COMPLETE TREATMENT FOR PREVENTION OF SCALING, CORROSION, AND FOULING.

FEATURES:

CONTROLS SCALE AND FOULING - Contains a combination of organic sequestrants and

synthetic polymers which act to keep heat exchange surfaces clean.

MINIMUM POLLUTION POTENTIAL - Does not impart toxic residues to cooling tower

bleed-off.  Does not contain Chromates, Phosphates, or other Heavy Metals.

ELIMINATES ACID FEED - Performance of this treatment does not depend on alkalinity

control.

ECONOMICAL AND CONVENIENT - This complete single treatment can be fed from the

shipping container.

APPLICATION:

RWT-32AD cooling water treatment is a multi-duty scale retardant, anti-foulant, and corrosion inhibitor in one complete product.  RWT-32AD was designed specifically to meet the requirements of cooling towers, evaporative condensers, and other open recirculating cooling water systems.  The excellent stability and non-aggressive nature of RWT-32AD permits its use in most normal temperature ranges and with all materials of construction.  RWT-32AD contains a unique blend of anti-foulants to prevent deposition and anti-nucleating agents to inhibit the formation of scale.

DOSAGE:

Approximately 1 pint to 1 quart of RWT-32AD for each 1,000 gallons of make-up water.

FEEDING:

RWT-32AD may be pumped directly from the shipping container into a recirculating cooling water line or directly to the tower basin.  A proportional feed and bleed system controlled by a conductivity monitor or a make-up water meter is recommended.

BLEED-OFF:

A Ryan representative will recommend the proper bleed-off according to individual specifications of the units to be treated.

SERVICE:

Regular service calls will be made.  Recommendations for changes in the treatment program will be made as the individual situation warrants.

PACKAGING:

30 gallon drums & 55 gallon drums.

"WATER TREATING CHEMICALS - WITH SERVICE"

# Text boxes

## Office: 800 - 345 – 7208

www.ryanchemical.com

# P.O. Box 406

Chandler, OK  74834

### RYAN CHEMICAL Co., Inc.