RY-1000

LIQUID ZINC ORTHOPHOSPHATE

POTABLE WATER SYSTEM CORROSION INHIBITOR

APPLICATION:   RY-1000 IS A CONCENTRATED LIQUID CORROSION INHIBITING FORMULATION,

DEVELOPED SPECIFICALLY FOR USE IN POTABLE WATER SYSTEMS, TO CONTROL

CORROSION OF DISTRIBUTION LINES, WATER HEATERS, AND OTHER CONTACTED

METAL SURFACES.

* CONTROL OF RED WATER.

* GIVES CORROSION CONTROL FOR IRON, COPPER, AND LEAD PIPING.

* REDUCE WATER MAIN FLUSHING TIME.

PROPERTIES:

COMPOSITION...........................................................................................................….......CLEAR  SOLUTION

SPECIFIC GRAVITY (at 700F).................................................................................…....................................1.28

FREEZING POINT(0F)...............................................................................................…......................................16

WEIGHT.....................................................................................................................…................10.6 LBS. / GAL.

ZINC CONTENT........................................................................................................…................0.88 LBS. / GAL.

ODOR...............................................................................................................…......NONE IN WATER SYSTEM

SOLUTION P.H. (AS SHIPPED).....................................................................…................................................1.2

FEEDING:                   RY-1000 MAY BE FED CONCENTRATED FROM DRUM OR MIXED WITH WATER.

DOSAGE:                    ALL DOSAGES AND APPLICATION POINTS ARE DETERMINED BY EVALUATING EACH

INDIVIDUAL WATER SYSTEM AND WATER QUALITY.

SAFE USAGE:            RY-1000 IS NSF CERTIFIED FOR SAFE USE IN DRINKING WATER.

HANDLING:               RY-1000 CAN BE HANDLED THE SAME AS ANY ACIDIC SOLUTION.  avoid CONTACT

WITH SKIN AND CLOTHING.   RY-1000 IN ITS CONCENTRATED FORM MAY CAUSE EYE

INJURY OR SKIN IRRITATION.  DO NOT GET IN EYES.  IN CASE OF CONTACT, FLUSH

WITH PLENTY oF WATER FOR 15 MINUTES AND GET IMMEDIATE MEDICAL

ATTENTION.

PACKAGING:           CONSULT YOUR LOCAL DISTRIBUTOR.

CASE HISTORIES:  YOUR AREA REPRESENTATIVE WILL BE GLAD TO SUPPLY REFERENCES FROM

WATER SUPPLIERS WHO ARE SUCCESSFULLY SOLVING THEIR INDIVIDUAL

PROBLEMS.

EXPERIENCE:           RYAN CHEMICAL HAS BEEN SERVING THE WATER TREATMENT INDUSTRY,

EXCLUSIVELY, SINCE 1955.  OUR RESEARCH AND DEVELOPMENT EFFORTS ARE

AIMED AT ONE PURPOSE - THE MOST COST EFFECTIVE TREATMENTS OFFERED

TODAY.  RYAN'S TECHNICAL PEOPLE ARE EXPERIENCED AND QUALIFIED TO SOLVE

ANY TREATMENT PROBLEMS OR ANSWER ANY QUESTIONS YOU MAY HAVE.

"WATER TREATING CHEMICALS - WITH SERVICE"

Printed 01-01-2016

# Text boxes

## Office: 800 - 345 - 7208

www.ryanchemical.com

# P.O. Box 406

Chandler, OK  74834

### RYAN CHEMICAL Co., Inc.